## Slide 1
6.1
Chapter 6
Bandwidth Utilization:
Multiplexing and Spreading
Copyright © The McGraw-Hill Companies, Inc. Permission required for reproduction or display.

## Slide 2
6.2
Bandwidth utilization is the wise use of available bandwidth to achieve specific goals.
Efficiency can be achieved by multiplexing; privacy and anti-jamming can be achieved by spreading.
Note

## Slide 3
6.3
6-1 MULTIPLEXING
Whenever the bandwidth of a medium linking two devices is greater than the bandwidth needs of the devices, the link can be shared. Multiplexing is the set of techniques that allows the simultaneous transmission of multiple signals across a single data link. As data and telecommunications use increases, so does traffic.
Frequency-Division Multiplexing Wavelength-Division Multiplexing Synchronous Time-Division Multiplexing
Statistical Time-Division Multiplexing
Topics discussed in this section:

## Slide 4
6.4
Figure 6.1 Dividing a link into channels

## Slide 5
6.5
Figure 6.2 Categories of multiplexing

## Slide 6
6.6
Figure 6.3 Frequency-division multiplexing

## Slide 7
6.7
FDM is an analog multiplexing technique that combines analog signals.
Note

## Slide 8
6.8
Figure 6.4 FDM process

## Slide 9
6.9
Figure 6.5 FDM demultiplexing example

## Slide 10
6.10
Assume that a voice channel occupies a bandwidth of 4 kHz. We need to combine three voice channels into a link with a bandwidth of 12 kHz, from 20 to 32 kHz. Show the configuration, using the frequency domain. Assume there are no guard bands.
Solution
We shift (modulate) each of the three voice channels to a different bandwidth, as shown in Figure 6.6. We use the 20- to 24-kHz bandwidth for the first channel, the 24- to 28-kHz bandwidth for the second channel, and the 28- to 32-kHz bandwidth for the third one. Then we combine them as shown in Figure 6.6.
Example 6.1

## Slide 11
6.11
Figure 6.6 Example 6.1

## Slide 12
6.12
Five channels, each with a 100-kHz bandwidth, are to be multiplexed together. What is the minimum bandwidth of the link if there is a need for a guard band of 10 kHz between the channels to prevent interference?
Solution
For five channels, we need at least four guard bands. This means that the required bandwidth is at least
5 × 100 + 4 × 10 = 540 kHz,
as shown in Figure 6.7.
Example 6.2

## Slide 13
6.13
Figure 6.7 Example 6.2

## Slide 14
6.14
Figure 6.9 Analog hierarchy

## Slide 15
6.15
Figure 6.10 Wavelength-division multiplexing

## Slide 16
6.16
WDM is an analog multiplexing technique to combine optical signals.
Note

## Slide 17
6.17
Figure 6.11 Prisms in wavelength-division multiplexing and demultiplexing

## Slide 18
6.18
Figure 6.12 TDM

## Slide 19
6.19
TDM is a digital multiplexing technique for combining several low-rate channels into one high-rate one.
Note

## Slide 20
6.20
Figure 6.13 Synchronous time-division multiplexing

## Slide 21
6.21
In synchronous TDM, the data rate of the link is n times faster, and the unit duration is n times shorter.
Note

## Slide 22
6.22

## Slide 23
6.23
In Figure 6.13, the data rate for each input connection is 1 kbps. If 1 bit at a time is multiplexed (a unit is 1 bit), what is the duration of (a) each input slot, (b) each output slot, and (c) each frame?
Solution
We can answer the questions as follows:
a. The data rate of each input connection is 1 kbps. This means that the bit duration is 1/1000 s or 1 ms. The duration of the input time slot is 1 ms (same as bit duration).
Example 6.5

## Slide 24
6.24
b. The duration of each output time slot is one-third of the input time slot. This means that the duration of the output time slot is 1/3 ms.
c. Each frame carries three output time slots. So the duration of a frame is 3 × 1/3 ms, or 1 ms. The duration of a frame is the same as the duration of an input unit.
Example 6.5 (continued)

## Slide 25
6.25
Figure 6.14 shows synchronous TDM with a data stream for each input and one data stream for the output. The unit of data is 1 bit. Find (a) the input bit duration, (b) the output bit duration, (c) the output bit rate, and (d) the output frame rate.
Solution
We can answer the questions as follows:
a. The input bit duration is the inverse of the bit rate: 1/1 Mbps = 1 μs.
b. The output bit duration is one-fourth of the input bit duration, or ¼ μs.
Example 6.6

## Slide 26
6.26
c. The output bit rate is the inverse of the output bit duration or 1/(4μs) or 4 Mbps. This can also be deduced from the fact that the output rate is 4 times as fast as any input rate; so the output rate = 4 × 1 Mbps = 4 Mbps.
d. The frame rate is always the same as any input rate. So the frame rate is 1,000,000 frames per second. Because we are sending 4 bits in each frame, we can verify the result of the previous question by multiplying the frame rate by the number of bits per frame.
Example 6.6 (continued)

## Slide 27
6.27
Figure 6.14 Example 6.6

## Slide 28
6.28
Four 1-kbps connections are multiplexed together. A unit is 1 bit. Find (a) the duration of 1 bit before multiplexing, (b) the transmission rate of the link, (c) the duration of a time slot, and (d) the duration of a frame.
Solution
We can answer the questions as follows:
a. The duration of 1 bit before multiplexing is 1 / 1 kbps, or 0.001 s (1 ms).
b. The rate of the link is 4 times the rate of a connection, or 4 kbps.
Example 6.7

## Slide 29
6.29
c. The duration of each time slot is one-fourth of the duration of each bit before multiplexing, or 1/4 ms or 250 μs. Note that we can also calculate this from the data rate of the link, 4 kbps. The bit duration is the inverse of the data rate, or 1/4 kbps or 250 μs.
d. The duration of a frame is always the same as the duration of a unit before multiplexing, or 1 ms. We can also calculate this in another way. Each frame in this case has four time slots. So the duration of a frame is 4 times 250 μs, or 1 ms.
Example 6.7 (continued)

## Slide 30
6.30
Figure 6.15 Interleaving

## Slide 31
6.31
Four channels are multiplexed using TDM. If each channel sends 100 bytes /s and we multiplex 1 byte per channel, show the frame traveling on the link, the size of the frame, the duration of a frame, the frame rate, and the bit rate for the link.
Solution
The multiplexer is shown in Figure 6.16. Each frame carries 1 byte from each channel; the size of each frame, therefore, is 4 bytes, or 32 bits. Because each channel is sending 100 bytes/s and a frame carries 1 byte from each channel, the frame rate must be 100 frames per second. The bit rate is 100 × 32, or 3200 bps.
Example 6.8

## Slide 32
6.32
Figure 6.16 Example 6.8

## Slide 33
6.33
A multiplexer combines four 100-kbps channels using a time slot of 2 bits. Show the output with four arbitrary inputs. What is the frame rate? What is the frame duration? What is the bit rate? What is the bit duration?
Solution
Figure 6.17 shows the output for four arbitrary inputs. The link carries 50,000 frames per second. The frame duration is therefore 1/50,000 s or 20 μs. The frame rate is 50,000 frames per second, and each frame carries 8 bits; the bit rate is 50,000 × 8 = 400,000 bits or 400 kbps. The bit duration is 1/400,000 s, or 2.5 μs.
Example 6.9

## Slide 34
6.34
Figure 6.17 Example 6.9

## Slide 35
6.35
Figure 6.18 Empty slots

## Slide 36: Data Rate Management
Assumption so far all input data rates are same
Disparity in input data rates?
Three strategies
  Multilevel Multiplexing
  Multiple-slot Allocation
  Pulse Stuffing
6.36

## Slide 37
6.37
Figure 6.19 Multilevel multiplexing

## Slide 38
6.38
Figure 6.20 Multiple-slot multiplexing
Multiple slot allocation is used to allot more than one slot in a frame to a single input line.

## Slide 39
6.39
Figure 6.21 Pulse stuffing
Pulse Stuffing is used to make the highest input data rate the dominant data rate and then add dummy bits to the input lines with lower rates

## Slide 40: Frame synchronization
Synchronization between the multiplexer and demultiplexer is a major issue in TDM.
Bit belonging to one chanel may be received by another.
Solution: Framing Bits
  Follows a pattern, frame to frame
6.40

## Slide 41
6.41
Figure 6.22 Framing bits

## Slide 42
6.42
We have four sources, each creating 250 characters per second. If the interleaved unit is a character and 1 synchronizing bit is added to each frame, find (a) the data rate of each source, (b) the duration of each character in each source, (c) the frame rate, (d) the duration of each frame, (e) the number of bits in each frame, and (f) the data rate of the link.
Solution
We can answer the questions as follows:
a. The data rate of each source is 250 × 8 = 2000 bps = 2 kbps.
Example 6.10

## Slide 43
6.43
b. Each source sends 250 characters per second; therefore, the duration of a character is 1/250 s, or 4 ms.
c. Each frame has one character from each source, which means the link needs to send 250 frames per second to keep the transmission rate of each source.
d. The duration of each frame is 1/250 s, or 4 ms. Note that the duration of each frame is the same as the duration of each character coming from each source.
e. Each frame carries 4 characters and 1 extra synchronizing bit. This means that each frame is 4 × 8 + 1 = 33 bits.
Example 6.10 (continued)

## Slide 44
The link sends 250 frames per second, and each frame contains 33 bits. This means that the data rate of the link is 250 × 33, or 8250 bps.
Note that the bit rate of the link is greater than the combined bit rates of the four channels. If we add the bit rates of four channels, we get 250x4x8= 8000 bps. Because 250 frames are traveling per second and each contains 1 extra bit for synchronizing, we need to add 250 to the sum to get 8250 bps.

## Slide 45: Example 6.11
Two channels, one with a bit rate of 100 kbps and another with a bit rate of 200 kbps, are to be multiplexed. How this can be achieved? What is the frame rate? What is the frame duration? What is the bit rate of the link?
Solution
We can allocate one slot to the first channel and two slots to the second channel. Each frame carries 3 bits. The frame rate is 100,000 frames per second because it carries 1 bit from the first channel. The bit rate is 100,000 frames/s × 3 bits per frame, or 300 kbps.

## Slide 46
6.46
Figure 6.23 Digital hierarchy
Telephone companies implement TDM through a hierarchy of digital signals, called digital signal (DS) service or digital hierarchy.
Digital Signal Service

## Slide 47
6.47
Table 6.1 DS and T line rates

## Slide 48
6.48
Figure 6.24 T-1 line for multiplexing telephone lines

## Slide 49
6.49
Figure 6.25 T-1 frame structure

## Slide 50
6.50
Table 6.2 E line rates
E LINES
Europeans use a version of T lines called E lines.
The two systems are conceptually identical, but their capacities differ..

## Slide 51
6.51
Figure 6.26 TDM slot comparison